Software Experiments 1 Report
Lim Liang Sun	1TE21133W

4. Display the statistics of inputted characters…..difficulty 2
# Let a user input characters (a to z) randomly within a fixed time.
# Count how many times each character (a to z) was inputted.
# Display a character with the largest number of inputs.

# Let a user input characters (a to z) randomly within a fixed time.
In the main function there is a loop that calls getstring then putstring continuously to allow users to type like in the echoback program.

# Count how many times each character (a to z) was inputted.
I allocated a space in the memory labelled ‘counters’ that is an array to store the frequency of each letter’s appearance. I extract the user input from the buffer and increment it with the head address of counters, to indicate which letter was pressed, then in that memory space byte, I increment 1. This process happens every user input that is between a-z in the ascii terms, 0x061 to 0x07a.

# Display a character with the largest number of inputs.
After 5 seconds, I execute another function TT using SET_TIMER function. In TT, I iterate through the counter memory address between a-z and collect the maximum number of appearance, and the memory address of it. Then finally I subtract the head counter addresss from the max=appearance address to obtain the ascii code of the most frequent letter. Which then I will pass onto the PUTSTRING function to be printed in the terminal.

Source code:

********************
** System call numbers
********************
    .equ SYSCALL_NUM_GETSTRING, 1
    .equ SYSCALL_NUM_PUTSTRING, 2
    .equ SYSCALL_NUM_RESET_TIMER, 3
    .equ SYSCALL_NUM_SET_TIMER, 4

******************************
** Head of the Register Group
*******************************
    .equ REGBASE, 0xFFF000 | DMAP is used.
    .equ IOBASE, 0x00d00000
*******************************
** Registers Related to Interrupts
*******************************
    .equ IVR, REGBASE+0x300 | Interrupt Vector Register
    .equ IMR, REGBASE+0x304 | Interrupt Mask Register
    .equ ISR, REGBASE+0x30c | Interrupt Status Register
    .equ IPR, REGBASE+0x310 | Interrupt Pending Register
*******************************
** Registers Related to the Timer
*******************************
    .equ TCTL1, REGBASE+0x600	|Timer1 Control Register
    .equ TPRER1, REGBASE+0x602	|Timer1 Prescaler Register
    .equ TCMP1, REGBASE+0x604	|Timer1 Compare Register
    .equ TCN1, REGBASE+0x608	|Timer1 Counter Register
    .equ TSTAT1, REGBASE+0x60a	|Timer1 Status Register
*******************************
** Registers Related to UART1 (Transmitter and Receiver)
*******************************
    .equ USTCNT1, REGBASE+0x900	|UART1 Status / Control Register
    .equ UBAUD1, REGBASE+0x902	| UART 1 Baud Control Register
    .equ URX1, REGBASE+0x904	| UART 1 Receiver register
    .equ UTX1, REGBASE+0x906	| UART 1 Transmitter Register
*******************************
** LED
*******************************
    .equ LED7, IOBASE+0x000002f	| Register for LED mounted on the board
    .equ LED6, IOBASE+0x000002d	| Refer to Appendix A.4.3.1 for a way to use
    .equ LED5, IOBASE+0x000002b
    .equ LED4, IOBASE+0x0000029
    .equ LED3, IOBASE+0x000003f
    .equ LED2, IOBASE+0x000003d
    .equ LED1, IOBASE+0x000003b
    .equ LED0, IOBASE+0x0000039
    .equ PUSHSW, 0xFFF419	| Register for Push Switch mounted on the board
****************************************************************
** Reservation of the stack region
****************************************************************
.section .bss
.even
SYS_STK:
    .ds.b 0x4000 | System stack region
    .even
SYS_STK_TOP: | End of the system stack region
****************************************************************
** Initialization
** A specific value has been set to internal device registers.
** Refer to each register specification in Appendix B to know the above reason.
****************************************************************
.section .text
.even
boot:
* Prohibit an interrupt into the supervisor and during performing various settings.
    move.w #0x2700, %SR	| run at lv.0
    lea.l SYS_STK_TOP, %SP | Set SSP
******************************
**Initialization of the interrupt controller
******************************
    move.b #0x40, IVR | Set the user interrupt vector number to 0x40+level.
    move.l #0x00ff3ff9, IMR | Allow UART1 and timer interrupts
    move.l #SYSCALL, 0x080 | Set the interrupt for system call TRAP #0
    move.l #INTERFACE, 0x110 | Set the interrupt subroutine for level 4 interrupt
    move.l #TIMER_INTERRUPT, 0x118 | Set the interrupt subroutine for level 6 interrupt
******************************
** Initialization related to the transmitter and the receiver (UART1)
** (The interrupt level has been fixed to 4.)
******************************
    move.w #0x0000, USTCNT1 | Reset
    move.w #0xe10c, USTCNT1 | Transmission and reception possible - no parity, 1 stop, 8 bit, allow only tranmission interrupt
    move.w #0x0038, UBAUD1 | baud rate = 230400 bps
*************************
** Initialization related to the timer (The interrupt level has been fixed to 6.)
*************************
    move.w #0x0004, TCTL1 | Restart, an interrupt impossible
        | Count the time with the 1/16 of the system clock
        | as a unit
        | Stop the timer use
    jsr	INIT_Q
bra MAIN

****************************************************************
** Program region
****************************************************************
MAIN:
    ** Set the running mode and the level (The process to move to 'the user mode')
    move.w	#0x0000, %SR	/*USER MODE, LEVEL 0*/
    lea.l	USR_STK_TOP, %SP	/*set user stack*/

    ** Start up RESET_TIMER by the system call
    move.l	#SYSCALL_NUM_RESET_TIMER, %d0
    trap	#0

    ** Start up SET_TIMER by the system call
    move.l	#SYSCALL_NUM_SET_TIMER, %d0
    move.w	#50000, %d1
    move.l	#TT, %d2
trap	#0

lea.l	BUF, %a2
move.l	#0, %d4

lea.l	counters, %a3
lea.l	counters, %a4
add.l	#123, %a4	/* a4 = end of array (z) */
add.l	#97, %a3	/* a3 = start of array (a) */
CLEAR:
move.b	#0, (%a3)+
cmp.l	%a3, %a4
bne	CLEAR

*************************************
* Test of sys_GETSTRING and sys_PUTSTRING
* Echo-back the input from a terminal
*************************************

LOOP:
    move.l	#SYSCALL_NUM_GETSTRING, %d0
    move.l	#0, %d1	/*ch = 0*/
    move.l	%a2, %d2	/*p = #BUF*/
    move.l	#1, %d3	/*size = 256*/
    trap	#0

cmpi.l	#0, %d0
beq	LOOP

move.b	#'1', LED1

move.b	(%a2), %d4
cmpi.b	#97, %d4	/* ascii for a*/
blt	Next
cmpi.b	#122, %d4	/* ascii for z */
bgt	Next

lea.l	counters, %a1
add.l	%d4, %a1
add.b	#1, (%a1)

move.b	#'0', LED0

Next:
    move.l	#SYSCALL_NUM_PUTSTRING, %d0
    move.l	#0, %d1	/*ch = 0*/
    move.l	#BUF, %d2	/*p = #BUF*/
    move.l	#1, %d3
trap	#0
move.b	#'2', LED2
    bra	LOOP

**************************************
* Test of the timer
* Display ‘******’ and CRLF (Carriage Return, Line Feed) five times
* Do RESET_TIMER after five times of the execution
**************************************

TT:
/* this subroutine happens at the end*/
movem.l	%d0-%d7/%a0-%a6, -(%sp)

GET_MAX:
lea.l	counters, %a0	/* load head address of counters*/
lea.l	counters, %a1

add.l	#97, %a1	/* start checking from 'a' */

move.l	#0, %d5	/* d5 = max freq. (no.) */
move.l	#0, %d4	/* i = 0 */
move.l	#0, %d6	/* d6 = max ascii (ascii) */

COMPARE:
addq	#1, %d4	/* increment counter */
cmp	#26, %d4	/* if counter > 26, leave */
bgt	DONE

cmp.b	(%a1), %d5	/* is current character the highest freq? */
bgt	SKIP

move.b	(%a1), %d5	/* !!!! d5 = Freq Max */
move.l	%a1, %a2	/* a2 = address containing max */

SKIP:
addq	#1, %a1	/* increment address */
bra	COMPARE

DONE:
move.l	%a2, %d6	/* get ascii code of max */
sub.l	%a0, %d6	/* !!!! d6 = Max ASCII */

PRINT:
lea.l	letter, %a3
move.b	%d6, (%a3)
    move.l	#SYSCALL_NUM_PUTSTRING, %d0
    move.l	#0, %d1	/*ch = 0*/
    move.l	#letter, %d2	/*p = #TMSG*/
    move.l	#1, %d3
    trap	#0

TTKILL:
move.l	#SYSCALL_NUM_RESET_TIMER, %d0
trap	#0

TTEND:
    movem.l	(%sp)+, %d0-%d7/%a0-%a6
    rts

****************************************************************
** System Call Interface:
**	Maker: Morris Kim, Rafii Hakim
** Reviewer: Lim Liang Sun, Napat Limsuwan
****************************************************************

SYSCALL:
cmpi.l	#SYSCALL_NUM_GETSTRING, %d0
beq	CALL_GETSTRING
cmpi.l	#SYSCALL_NUM_PUTSTRING, %d0
beq	CALL_PUTSTRING
cmpi.l	#SYSCALL_NUM_RESET_TIMER, %d0
beq	CALL_RESET_TIMER
cmpi.l	#SYSCALL_NUM_SET_TIMER, %d0
beq	CALL_SET_TIMER
rte

CALL_GETSTRING:
jsr	GETSTRING
rte
CALL_PUTSTRING:
jsr	PUTSTRING
rte
CALL_RESET_TIMER:
jsr	RESET_TIMER
rte
CALL_SET_TIMER:
jsr	SET_TIMER
rte

****************************************************************
**	Timer interrupt
**	Maker: Lim Liang Sun, Napat Limsuwan
** Reviewer: Morris Kim, Rafii Hakim
****************************************************************
TIMER_INTERRUPT:
movem.l	%a0, -(%sp)	/* Evacuate registers */
cmp	#0, TSTAT1	/* Checks 0th bit of TSTAT1 */
beq	TIMER_INTERRUPT_END
clr.w	TSTAT1	/* Reset TSTAT1 to 0 */
jsr	CALL_RP
TIMER_INTERRUPT_END:
movem.l	(%sp)+, %a0
rte

RESET_TIMER:
move.w	#0x0004, TCTL1	/* Restart, an interrupt impossible, input is SYSCLK/16, prohibit timer */
rts
SET_TIMER:
/* D1.W = t (timer interrupt cycle, every 0.t msec) */
/* D2.L = p (head address of the routine to be called at the interrupt occurrence) */
/* STILL NEED TO DEFINE GLOBAL VARIABLE TASK_P IN THE .BSS SECTION */
move.l	%d2, task_p	/* Substitute p for the global variable task_p*/
move.w	#0x00CE, TPRER1	/* Let counter increment by 1 every 0.1 msec*/
move.w	%d1, TCMP1	/* Substitute t for the TCMP1 */
move.w	#0x0015, TCTL1	/* Restart, enable compare interrupt, input is SYSCLK/16, permit timer */
rts
CALL_RP:
move.l	(task_p), %a0
jsr	(%a0)
rts

****************************************************************
**	UART1 Interrupt Interface
**	Maker: Morris Kim, Rafii Hakim
** Reviewer: Lim Liang Sun, Napat Limsuwan
****************************************************************
INTERFACE:
movem.l	%d0-%d3,-(%sp)

/* Receiver Interrupt */
move.w	URX1, %d3	/* Copy register URX1 to %d3.w*/
btst.l	#13, %d3	/* Receiver FIFO? 1 = not empty, 0 = empty, yes it's confusing*/
bne	CALL_INTERGET	/* Basically, this checks if it is a receiver interupt*/

/* Transmitter Interrupt */
move.w	UTX1, %d3
btst.l	#15, %d3	/* Transmitter FIFO empty? 1 = empty, 0 = not empty*/
bne	CALL_INTERPUT	/* not equal to 1*/

INTERFACE_END:
movem.l	(%sp)+, %d0-%d3
rte

CALL_INTERPUT:
move.l	#0, %d1
jsr	INTERPUT
bra	INTERFACE_END

CALL_INTERGET:
move.l	#0, %d1
move.b	%d3, %d2	/* Copy lower 8 bits (data part) of %d3.w to %d2.b*/
jsr	INTERGET
bra	INTERFACE_END

****************************************************************
**	INTERGET
**	Maker: Zelal Denis Yildiz
** Reviewer: Amira Ben Youssef
****************************************************************
INTERGET:
/* Input: Channel ch -> %d1, received data -> %d2 */
/* No return value */
/* Do we have to save running level??? */
movem.l	%d0, -(%sp)

cmpi.l	#0, %d1
bne	INTERGET_END

move.l	#0, %d0	/* Queue #0 */
move.b	%d2, %d1	/* move data to d1*/
jsr	INQ	/* Do we have to do something for INQ failure?? */

INTERGET_END:
movem.l	(%sp)+, %d0
rts

****************************************************************
** INTERPUT
**	Maker: Amira Ben Youssef
** Reviewer: Zelal Denis Yildiz
****************************************************************
INTERPUT:
/* Input: Channel ch -> %d1 */
/* d0 = UTX1 at the end, we need %d0 to compare when we return to INTERFACE*/
/* No return value */

movem.l	%d2/%a1,-(%sp)
move.w	%SR, %d2	/* Save running level */
move.w	#0x2700, %SR	/* Set running level to 7 */
cmp.l	#0, %d1	/* Return without doing anything if ch=/=0*/
bne	INTERPUT_END

move.l	#1, %d0	/* Queue #1 */
jsr	OUTQ	/* Substitute it for data?? */
/* d1 is data */

cmp.l	#0, %d0	/* OUTQ failure? */
beq	MASK_TRANSMITTER_INTERRUPT

add.l	#0x0800, %d1
move.w	%d1, UTX1	/* Substitute the data for the transmitter register UTX1 */
bra INTERPUT_END

MASK_TRANSMITTER_INTERRUPT:
andi	#0xfff8, USTCNT1 /* Mask the transmitter interrupt */
INTERPUT_END:
move.w	%d2, %SR	/* Restore running level */
movem.l	(%sp)+, %d2/%a1
rts

****************************************************************
** PUTSTRING
**	Maker: Amira Ben Youssef
** Reviewer: Zelal Denis Yildiz
****************************************************************
PUTSTRING:
/* Input: Channel ch -> d1, Head address p -> d2, No. of data -> d3 */
/* Output: no. of data actually sent -> d0 */
movem.l	%d4/%a0, -(%sp)
cmp.l	#0, %d1
bne	PUTSTRING_END	/* If ch =/= 0, end */

move.l	#0, %d4	/* d4 = sz */
move.l	%d2, %a0	/* a0 = i */

cmp.l	#0, %d3
beq	PUTSTRING_UPD_SZ

PUTSTRING_LOOP:
cmp.l	%d4, %d3	/* If sz == size */
beq	PUTSTRING_UNMASK

move.b	(%a0)+, %d1	/* Put data in d1 */
move.l	#1, %d0	/* Use queue 1 */
jsr	INQ

cmp.l	#0, %d0	/* If INQ failed*/
beq	PUTSTRING_UNMASK

addq	#1, %d4	/* Increment sz and i */

bra	PUTSTRING_LOOP

PUTSTRING_UNMASK:
ori	#0x0007, USTCNT1	/* Permit the transmitter interrupt */

PUTSTRING_UPD_SZ:
move.l	%d4, %d0	/* %d0 <- sz */

PUTSTRING_END:
movem.l	(%sp)+, %d4/%a0
rts

****************************************************************
** GETSTRING
**	Maker: Zelal Denis Yildiz
** Reviewer: Amira Ben Youssef
****************************************************************
GETSTRING:
/* Input: ch -> d1, head address of destination p -> d2, no. of data to be read -> d3 */
/* Output: no. of data actually read out -> d0 */
movem.l	%d4/%a0, -(%sp)

cmpi.l	#0, %d1
bne	GETSTRING_END	/* If ch =/= 0, end */

move.l	#0, %d4	/* d4 = sz (Used to count no. of data actually read out) */
move.l	%d2, %a0	/* a0 = i (NOT Index, but head address of destination) */

GETSTRING_LOOP:
cmp.l	%d4, %d3	/* is sz == size? */
beq	GETSTRING_UPD_SZ

move.l	#0, %d0	/* specify queue 0 */
jsr	OUTQ	/* Call OUTQ, puts data in d1 */

cmpi.l	#0, %d0	/* If failure */
beq	GETSTRING_UPD_SZ	/* End GETSTRING */

move.b	%d1, (%a0)+	/* Copy the data to address i */

addq	#1, %d4	/* Increment sz and i */
jmp	GETSTRING_LOOP

GETSTRING_UPD_SZ:
move.l	%d4, %d0	/* %d0 <- sz */

GETSTRING_END:
movem.l	(%sp)+, %d4/%a0
rts

*****************************************************************
** Queues
**	Maker: Amira Ben youssef, Zelal Denis Yildiz
** Reviewer: Moris Kim
*****************************************************************
INIT_Q:
movem.l	%a1-%a4, -(%sp)

lea.l	top, %a1	/*top address is a1*/
lea.l	inp, %a2
lea.l	outp, %a3
lea.l	s, %a4

move.l	%a1, (%a2)+ /* Initialize inp, outp, and s for q0*/
move.l	%a1, (%a3)+
move.w	#0, (%a4)+

adda	#SIZE_of_QUEUE, %a1 /* add offset for q1 */

move.l	%a1, (%a2) /* Initialize inp, outp, and s for q1*/
move.l	%a1, (%a3)
move.w	#0, (%a4)

movem.l	(%sp)+, %a1-%a4
rts

INQ:
/* Input: Queue no. -> %d0, Data -> %d1 */
/* Output: Success/fail -> %d0 */
movem.l	%d2-%d5/%a1-%a5,-(%sp) /* Save registers */

jsr	Q_START
lea.l	inp, %a2	/* inp -> a2 */
adda.l %d2, %a2 /* add offset */
move.l (%a2), %a1 /* a1 = in pointer */

jsr	INQ_SIZE_CHECK
jmp	Q_FINISH

INQ_SIZE_CHECK:
cmp.w	#256, (%a3) /* check if queue is full */
bne	INQ_SUCC	/*if s not equals to 256*/
bra	Q_FAIL	/*if s==256*/

INQ_SUCC:
move.b	%d1, (%a1) /* d1 = data moved into inp */
addq #1, (%a3) /* Increment size */

jmp Q_SUCC

OUTQ:
/* Input: Queue no. -> %d0 */
/* Output: Success/fail -> %d0, Data -> %d1 */
movem.l	%d2-%d5/%a1-%a5,-(%sp) /* Save registers */
jsr Q_START
lea.l	outp, %a2	/* outp -> a2 */
adda.l %d2, %a2 /* add offset */
move.l (%a2), %a1 /* a1 = out pointer */

jsr	OUTQ_SIZE_CHECK
jmp	Q_FINISH

OUTQ_SIZE_CHECK:
cmp.w	#0, (%a3) /* check if queue is empty*/
bgt	OUTQ_SUCC
bra	Q_FAIL

OUTQ_SUCC:
move.b	(%a1), %d1 /* data is moved to d1*/
subi.w #1, (%a3) /* Decrement size */

jmp	Q_SUCC

/* These are common for both INQ and OUTQ */
Q_START:
move.w	%SR, %d5 /* Save running level */
move.w	#0x2700, %SR	/* running level = 7 */

move.l	%d0, %d2 /* d2 = pointer offset */
mulu	#4, %d2 /* because address is stored in longword */

move.l %d0, %d3 /* d3 = queue size pointer offset */
mulu	#2, %d3	/* because address is stored in word */

lea.l	s, %a3 /* size -> a3 */
adda.l %d3, %a3 /* add offset */
rts

Q_SUCC:
move.l	%d0, %d4 /* d4 = queue area offset */
mulu	#SIZE_of_QUEUE, %d4
lea.l top, %a4 /* a4 = head of queue area */
adda.l %d4, %a4 /* adds offset */
move.l %a4, %a5 /* a5 = bottom of queue area */
adda.l #255, %a5 /* the bottom is 255 from the top */

move.l #1, %d0 /* success flag raised */

cmp	%a1, %a5	/* compare inp/outp with bottom*/
beq	Q_BACK	/* reach the bottom */
bra	Q_NEXT

Q_NEXT:
addq	#1, %a1 /* increment input/output pointer*/
rts

Q_BACK:
move.l	%a4, %a1 /* input/output pointer set to head of queue area */
rts

Q_FAIL:
move.l	#0, %d0 /* set flag to fail */
rts

Q_FINISH:
move.l	%a1, (%a2) /* update inp/outp */
move.w	%d5, %SR /* restore previous running level */
movem.l	(%sp)+,%d2-%d5/%a1-%a5 /* restore registers */
rts

****************************************************************
**	Data region with an initial value
****************************************************************
.section .data
.equ	SIZE_of_QUEUE,	256

TMSG:	.ascii	"******\r\n"
        .even
TTC:	.ascii	"######\r\n"
        .even

****************************************************************
**	Data region without an initial value
****************************************************************
.section .bss
BUF:	.ds.b	256
        .even
USR_STK:
        .ds.b	0x4000
        .even
USR_STK_TOP:
.even
top:	.ds.b	SIZE_of_QUEUE*2
inp:	.ds.l	2
outp:	.ds.l	2
s:	.ds.w	2
task_p:	.ds.l	1
max_freq:	.ds.b	1
letter:	.ds.b	1
counters:	.ds.b	97 + 26
        .even